## Slide 1: MSIS LAB
Introduction To
MSIS Lab Research (V2X for Self Driving)
2018. 05
Prof. HyungWon Kim
MSIS LAB
Department of Electronics Engineering
Chungbuk National University

## Slide 2: MSIS Lab’s Research (Wireless & Deep Learning)
Deep Learning AI & Image Recognition
◇ Object and Environment Recognition for Smart Car (Autonomous Vehicle)
◇ Multi-Sensor Fusion Algorithm for Vehicle Tracking Enhancement
◇ Multi-Vehicle Senor Fusion Using V2X (Vehicle-to-Anything) Communication
◇ Moving Object Detection, Classification, Identification, Tracking with Fast CNN (Convolutional Neural Network)
◇ Low Power & Compact Neural Network Algorithm for IoT (Internet of Things)
◇ Image Recognition for IoT Sensors (Wireless Metering, Environment monitor)
◇ Embeded Programming on ARM Cortex M4, Cortex A9, with RTOS, Linux
Smart Car V2X Network & Wireless Sensor Network
◇ Enhanced V2X Network for transmitting Sensor data & Safety Decision
Inforamtion between Smart Cars (Autonomous Vehicles)
◇ Multi-Hop Reliable Broadcast with TDM Scheduling for High speed, low latency, guaranteed delivery of congested V2X networks
◇ Wide-Range LDM (Local Dynamic Map) Generation and transmission method
◇ Automonous driving safety decision algorithms using Wide-Range LDM:
FCW (Forward collision warning), LCW (Lane change warning), EEBL (Electronic
Emergency Brake), IMA (Intersection Movement Assist), LTA (Left Turn Assist)

## Slide 3: V2X: Applications for Connected Car
Collision avoidance: V2I & V2V (V2X)
Cloud service: V2N
Pedestrian safety: V2P

## Slide 4: V2X Standard in US: Planned Mandates

## Slide 5: V2X Standards Trend & Projection
US: WAVE/DSRC
EU: ETSI/C-ITS (G5)
Cellular: 3GPP/C-V2X (LTE/5G /w D2D)
WAVE
+
C-ITS
WAVE+
C-ITS
+
C-V2X
2002
2012
2016
2019
2023
Consolidation
Consolidation
5.9GHz
Allocation
IEEE
802.11p
Released
IEEE 1609
V2X Law
Enforced
V2X
Equipped
Cars
Release1
Release2
Celluar-V2X
Standard
Group (R12)
Release
R14
Release
R17
Deployed

## Slide 6: Limitation of Current V2X

## Slide 7: Enhancing V2X: Multi-hop & Sensing Fusion
Smart V2X Network for Wider Coverage
Problem: Single Car Sensing ADAS  Limits Autonomous Vehicles only to low speed
Problem: Using current V2X Standard  Slow down the adoption of V2X and autonomous cars
Solution: Adaptive Multi-Hop LDM Propagation  Guarantee large scale V2X coverage Multi-Car Sensing Data Fusion  Accurate LDM for Wider Coverage
Problem: Short Range Coverage of only Positions
Goal: Intelligent Wide Range Mobility Map
Enhancement:
Multi-Hop LDM+ Sensing Fusion

## Slide 8: Development Platform for Enhanced V2X with Sensing Fusion
V2X/GPS Antenna
(Cohda MK5 V2X)
Target Platform: In-Vehicle Sensors: Cameras, Lidar, Radar, IMU sensors
LDM Generation
Veh. Path Prediction
IEEE1609/802.11p Protocol
Linux OS
TX/RX BSM
packets
V2X Safety App S/W
TCP/IP
To ECUs
V2X H/W & S/W Architecture
V2X Software Architecture
V2X OBU Module
Multi-Hop
V2X Protocol

## Slide 9: Target V2X Software Structure
IEEE 802.2 LLC Sublayer
IEEE 1609.4 MAC Sublayer Extension
IEEE 802.11p MAC Sublayer
IEEE 802.11p PHY Sublayer
IEEE 1609.2
Security Service
Adaptive non-linear random DCF back-off mechanism
  Multi-Hop Broadcaster Selection (Collision Reduction)
Enhanced priority scheme to expedite safety application processing
Dynamic TDMA based Collision avoidance
Adaptive cross layered control mechanism to fit in WAVE and C-ITS
Adaptive TDM Code Allocation (Collision-Free)
Emergency Electronic Braking Lights(EEBL)
Blind Spot / Lane Change Warning (BSW/LCW)
Forward Collision Warning(FCW)
Do Not Pass Warning(DNPW)
Intersection Movement Assistant(IMA)
Left Turn Assist(LTA)
Reduced Speed Zone Warning(RSZW)
Curve Speed Warning(CSW)
Red Light Violation Warning(RLVW)
Develop:
V2X Safety
Application
Layer
Develop:
WAVE
Enhancement
Protocol
Enhanced V2X Safety Applications Mandated by US NHTSA

## Slide 10: V2X Safety Application 1: FCW (Forward Collision Warning) Prediction
Current State : denoted as TTC (Time To Collision).
  The time before collision if no actions taken.
Course change state: denoted as Stopping time.
  The time taken by HV to stop if brakes are applied
Position vector of RV in time ,
At least one of or is a null vector.

## Slide 11: V2X Safety Application 2: EEBL (Electronic Emergency Brake Light) Warning
Four vehicles are moving to righthand direction with different speed.
Each vehicle is equipped with collision warning system.
RV3 uses EEBL to avoid the collision
Once RV2, RV1 and HV receive EEBL message, they will take proper action to avoid the collision.
Since RV1 and RV2 has shorter distances to RV3, they change the lane.
HV spots after having enough space.
Then RV2 detects the object on his lane, it uses EEBL to avoid the crash.
RV1 has high speed and short space to stop and it changes its lane to avoid the collision.

## Slide 12: V2X Safety Application 2: Test Result EEBL (Electronic Emergency Brake Light) Warning
EEBL Ported on to V2X Hardware
Emulation Demo with VSIM and 3 V2X modules

## Slide 13: V2X Safety Application 2: Lane Change Warning (LCW)
Lane change warning depends on
  Initial distance between HV and RV ().
  Speed and acceleration of HV and RV: If safe to lane change, we can give advisory for minimum speed.
Distance travelled by RV in ,
Distance travelled by HV in the same time,
The effective distance traversed by HV in road direction is
For safe LC effective distance should follow following condition
After time

## Slide 14: LCW Test Result: When the Next Lane is Available

## Slide 15: Generate LDM (Local Dynamic Map)
LDM:
  Updates vehicle status upon received BSM
  Provides up-to-date information to BSM generation function.
  Executes self-estimation to purge aged information

## Slide 17: Virtual Drive Test Tool (HIL Simulator)
VSIM: Route creation, Synthesized GPS for multi vehicles
Multi-Vehicle Emulation with Multiple V2X Modules
V2X Protocol & Safety App Running on Each V2x Module
Visualizer Tool shows LDM of each Vehicle (V2X)