## Slide 1: On-Chip Voltage Scaler Circuits with Energy-Efficient Charging and Recycling
Prof. HyungWon Kim
Dept. of Electronic Engineering,
College of Electrical Engineering and Computer Science,
Chungbuk National University
MSIS

## Slide 2: Research Goal of Low Power Voltage Scaler
On-Chip Dynamic Voltage Scaler for Multiple Power Domain
  Dynamic Power Management For Multiple micro-grain power domains
  Wide input and output voltage range
  On-Demand Dynamic output voltage scaling
  Small form factor On-chip Switched Capacitor Voltage converter and Scaler

## Slide 3: Conventional Voltage Converters
Inductor Based DC-DC Converters (Buck Converter)
Linear Voltage Regulator: LDO (Low Drop Out)
Layout of 5.5 nH inductor with area of (354.08 µm)2

## Slide 4: Switched Capacitor (SC) DC-DC Converters
Requirements for On-Chip DC-DC Converters and Regulators
  Multicore processors dissipate power in the range of 1 W/mm2
  Integrated dc–dc conversion requirements:
  Steps down from a conveniently chosen voltage above typical CMOS core operating voltages;
  Provides high efficiency over a wide load and voltage range;
  Highly scalable for granular implementation
Problems of Inductor DC-DC Converters
  High-power requires intensive integrated inductor or a bulky off-chip inductor
  Transistors rated for the full input voltage and the full output current of the application
Advantage of SC Converters
  Requires only capacitors as passives
  Capacitors have significantly higher energy and power densities
  More easily integrated than inductors
Drawback of SC Converters
  Limited to low-power (<100 mW) applications
  High ripple voltages & relatively large output voltage granularity
  On-chip capacitors still requires large chip area
Additional Benefits of SC Converters
  NMOS Switches need about 1 V rating (whereas buck converters need 10 V rating)
  No inductive switching losses, and less overshoots, body diode conduction, and less timing issues
  Low-power operation without control complexity, reducing clock rate.
  Higher Energy density of capacitors, orders of magnitude greater than inductors.

## Slide 5: Switched Capacitor (SC) DC-DC Converters
Switched Capacitor Voltage Converter Types
Dickson Star Converter
Ladder (Variation) Converter
Five Step-Up Converters Compared
  (a) Ladder
  (b) Cockcroft-Walton Multiplier (Dickson Variation)
  (c) Fibonacci
  (d) Series-Parallel (or Parallel Series)
  (e) Doubler

## Slide 6: Target Architecture of Dynamic Voltage Scaler
Target Dynamic Voltage Scaler Structure
Main Blocks and Path of DVS
  Voltage Converter and Storage Analog Block
1st Stage
  Reconfigurable Voltage Buck-Boosting Energy Storage
  Reconfigurable Coarse level Voltage Output
2nd stage
  ULP Switched-Capacitor Voltage Regulator block
  Minimize Voltage ripple to further reduce energy waste
DVS feedback controller block
  Output voltage feedback circuit
    DVS output voltage의 measurement
  Ultra Low Powr comparator Circuit
    Compare with the target Reference voltage
  Dynamic feedback controller
    With Comparator’s result, control the Energy storage and Voltage regulator
  Low power PLL (Phase Locked Loop) clock generator
    Provide control clocks to Energy storage and Voltage regulator
Reconfigurable Voltage Boosting
Energy Storage
ULP Switched-Capacitor Voltage Regulator
Output
Voltage
Feedback
Circuit
Vctrl
DVS Output
Low Energy Loss Dynamic Voltage Scale Controller Architecture
Low Power
Clock Generator
(PLL)
ULP Subthreshold
Comparator
Input
Voltage Source
Dynamic
Voltage
Feedback
Controller
Vref
Voltage Converter and Storage Analog Block
DVS Feedback Controller Block
Voltage Level Selection from Main Power Management

## Slide 7: An Energy Efficient Charging Technique for Switched Capacitor Voltage Converters with Low Duty-Ratio
Saad Arslan, Syed Asmat Ali Shah, HyungWon Kim
Dept. of Electronic Engineering,
College of Electrical Engineering and Computer Science,
Chungbuk National University
MSIS

## Slide 8: Target Applications: Low Duty Ratio Operation
A circuit is active for a small period of time
  Followed by a long sleep period
Problems of dynamic power
  Suffer with poor energy efficiency
  Due to losses in transition periods
During sleep-to-active transition
  DC-DC converter’s capacitor bank is charged
  From zero to a certain voltage
In Switched-Capacitor (SC) DC-DC converter
  The initial charging is done at 50% energy efficiency
  Half the energy from the source is wasted and only half is stored in capacitors

## Slide 9: Initial Charging of an SC DC-DC Converter (1/2) -Conventional Converter (One-Step Charging)

## Slide 10: Initial Charging of an SC DC-DC Converter (2/2) -Two Step Charging
Conventional (one-step charging)
Two-step charging
Simulation results by using mathematical model in MATLAB
Using additional charging stage
Efficiency of step 1 & 2 is
  𝜂1= 50% and 𝜂2=75%
Total charging efficiency 𝜂=66.67%
By adding more charging steps, efficiency can be further improved

## Slide 11: Initial Charging of an SC DC-DC Converter -Split-Capacitor Charging (Four-Step Charging)
Splitting each capacitor into smaller units, allow more charging steps
By splitting each into three
  Four-step charging is obtained
  With charging efficiency of 75%
  66.67% reduction in energy wastage
Proposed six capacitor bank
Architecture
Configurations during each charging step
Six capacitor, four-step split-capacitor charging simulation.

## Slide 12: Initial Charging of an SC DC-DC Converter -Comparison of N-Step Charging
The table shows summary of MATLAB simulation results
  For various number of charging steps (including split-capacitor charging),
  Showing total efficiency, efficiency of each step and capacitor configuration
 | Total | Charging Steps |  |  |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Capacitors | 1 | 1,1 |  |  |  |  |  |  | 
Efficiency | 49.9% | 49.9% |  |  |  |  |  |  | 
Capacitors | 2 | 1,2 | 2,1 |  |  |  |  |  | 
Efficiency | 66.6% | 49.9% | 75.0% |  |  |  |  |  | 
Capacitors | 4 | 1,4 | 2,2 | 4,1 |  |  |  |  | 
Efficiency | 72.7% | 49.7% | 75.0% | 75.0% |  |  |  |  | 
Capacitors | 6 | 1,6 | 2,3 | 3,2 | 6,1 |  |  |  | 
Efficiency | 75.0% | 49.6% | 75.0% | 83.3% | 75.0% |  |  |  | 
Capacitors | 8 | 1,8 | 2,4 | 4,2 | 8,1 |  |  |  | 
Efficiency | 74.4% | 49.5% | 74.9% | 75.0% | 75.0% |  |  |  | 
Capacitors | 12 | 1,2 | 2,6 | 3,4 | 4,3 | 6,2 | 12,1 |  | 
Efficiency | 76.6% | 49.2% | 74.9% | 83.3% | 87.5% | 83.3% | 75.0% |  | 
Capacitors | 24 | 1,24 | 2,12 | 3,8 | 4,6 | 6,4 | 8,3 | 12,2 | 24,1
Efficiency | 77.0% | 48.5% | 74.8% | 83.3% | 87.5% | 83.3% | 87.5% | 83.3% | 75.0%
*Capacitors arrangement represented as
(Number of Branches, Number of series capacitors in each branch)

## Slide 13: Schematic Simulation One-Step vs. Split-Cap. Charging
Compares Charging behavior of Split-Capacitor Charging (four-step)
  With one-step charging
Split-Cap. Charging outperforms, by providing 73.73% efficiency
  Reducing energy wastage by 65.51%
  With only 20% overhead of charging period

## Slide 14: Split-Cap. Charging Based Boost Converter
Simulation results show
  Improvement for short active periods
  By incorporating Split-Cap. Charging
Boost Converter for an active period of ten clock cycles
Comparison of Split-Cap. Vs. one-step charging
for various lengths of active periods

## Slide 15: Viability of MEMS Switches in SC DC-DC Converter
To evaluate the viability, following five scenarios are used
  All MOSFET switches
  Input switch is ideal (MEMS), rest are MOSFETs
  Output switch is ideal (MEMS), rest are MOSFETs
  Both Input and output switches are ideal (MEMS), rest are MOSFETs
  All switches are ideal (MEMS)
Non-overlapping signals are used to minimize switching losses
Act. Period (# cycles) | All are MOSFET SW | Only Input is Ideal SW | Only Output is Ideal SW | Both In/Output are Ideal SW | All are Ideal SW
20 | 69% | 71.96 | 69.55% | 72.97% | 72.12%
40 | 73.73% | 76.85% | 74.37% | 77.98% | 79.38%
250 | 80.35% | 83.46% | 81.12% | 84.77% | 89.34%
500 | 81.2% | 84.29% | 81.98% | 85.62% | 90.6%
1000 | 81.65% | 84.72% | 82.43% | 86.06% | 91.25%
*Using Split-Cap. Chrg. & Energy Recycling converter

## Slide 16: Energy Recycling Voltage Scaler Based on Reconfigurable Capacitive Array
Syed Asmat Ali Shah, Saad Arslan, *HyungWon Kim
Dept. of Electronic Engineering, College of Electrical Engineering and Computer Science, Chungbuk National University
MSIS

## Slide 17: Combining Split Charging and Energy Recycling
Capacitor Bank with Reconfigurable switches
Overall Circuit Structure
  Proposed Architecture
  Capacitor Bank

## Slide 18: Combining Split Charging and Energy Recycling
Cadence Virtuoso Layout
Capacitor Bank (190 m x 70 m)
(Six Capacitors)
Digital Control Circuit
Comparator
Switches
  Layout of the Proposed Architecture.

## Slide 19: Efficiency Improvement by SCC and ER
For maximum power saving both the transitions should be optimized. i.e. SCC and ER
  Relative gain of SCC and ER compared to conventional SC DC-DC converters

## Slide 20: Proposed Architecture As a Buck Converter
  Split Cap. Charging Configurations
  Energy Recycling Configurations
For generating a target voltage ratio of 2/3 𝑉𝑖𝑛 , the capacitors are charged in two steps.
  All of the capacitors are in series.
  Two branches having three series capacitors.
Energy Recycling will be carried out in three steps.
  First configuration three branches each having two series capacitors.
  Second configuration two branches having three series capacitors.
  Third configuration one branch having six series capacitors

## Slide 21: Proposed Architecture As a Boost Converter
  Split Cap. Charging Configurations
  Energy Recycling Configurations
For generating a target voltage ratio of 2Vin , the capacitors are charged in four steps.
  All of the capacitors are in series.
  Two branches having three series capacitors.
  Three branches having two series capacitors.
  Six branches having one capacitor in each branch.
Energy Recycling will be carried out in three steps. (Same as Buck)

## Slide 22: Energy Model for Energy Recycling Steps
Remaining Energy in Each Recycling Steps
  Initial Energy After Charging:
  General Form of Remaining Energy :
  Energy Recycling Step1:
  Energy Recycling Step2:
  Energy Recycling Step3:

## Slide 23: Simulation Results of Energy Recycling Steps
Simulation results with an active period of 6 addition operations followed by a long sleep period
  Energy Recycling Voltage Converter
  Conventional Voltage Converter

## Slide 24
Fig. compares the simulation results for MOSFET and MEMS switches at the input and output of the proposed architecture.
MOSFET Switches
  Charging Efficiency =
  Recycling Efficiency = .
  MEMS Switches
  Charging Efficiency = .
  Recycling Efficiency =
  Simulation results with (a) real transistors (b) Ideal switches.
Viability of MEMS Switches in SC DC-DC Converter For short Active period Charge & Recycle (Light Load)

## Slide 25
Fig. compares the simulation results for MOSFET and MEMS switches at the input and output of the proposed architecture.
MOSFET Switches
  Charging Efficiency =
  Recycling Efficiency = .
  MEMS Switches
  Charging Efficiency = .
  Recycling Efficiency =
  Simulation results with (a) real transistors (b) Ideal switches.
Viability of MEMS Switches in SC DC-DC Converter
For short Active period Charge & Recycle (Heavy Load)

## Slide 26: Viability of MEMS Switches in SC DC-DC Converter -Conclusion
Initial Charging
  For charging capacitor bank using ideal switches will not give any additional benefits.
  Because during charging a capacitor resistance (R) doesn’t impact energy.
For Continuous phase
  It shows improvement in energy efficiency
  The charging is done quickly which reduces losses while delivery to load
  Energy Recycling
  For Energy recycling for higher current (Heavy Load), we can have some improvements in efficiency.
However, a much higher operating frequency of the MEMS switches is needed
  To make them useable in low power circuits

## Slide 27: Voltage Scaler Test Chip MPW
MPW Process: Magnachip CMOS 0.13um 1.5V Vdd.
  Chip Size 5x5mm
  Voltage Scaler Test Chip
  Voltage Scaler Test Chip